## Slide 1: Start the journey to Internet of Things with Arduino
Pradeep Bhatter
@Pbhatter, pbhatter@yahoo.com
Notes: Introduction
Kids: Grade level, Programming experience, Electric & Electronic circuits
https://www.youtube.com/watch?v=VQj71FWk1FA Harold Robins Help!
https://www.youtube.com/watch?v=PdBvBtdbQpw 3 Stoogies
https://www.youtube.com/watch?v=l-gQLqv9f4o pep talk

## Slide 2: Ground rules
Participate and enjoy; Share, work as a team.
Be Safe!
Getting attention: If your team needs help, make the red cup visible. Otherwise keep the green cup visible.
This is a work area! People are working. Please do not disturb them.
Use the kits carefully and re-assemble it back at the end of the workshop. Other teams will use them.
One parent can help the team, if needed.
Rest rooms are by the break room.
Notes: Kits used today will be sold after the afternoon session at cost.

## Slide 3: New gadgets ….

## Slide 4: New gadgets ….

## Slide 5: Have you seen this one ….

## Slide 6: Joining hands …
Internet of Things
Sensors
Controllers
Wireless &
Network
Apps
Mobile devices
Cloud

## Slide 7: What are we going to do today?
Use electricity to sense and change the world around us.
Connect sensors and actuators to controller (Arduino) and make “Things”
Write instructions for Arduino to provide “behavior” to “Things”
Communicate with “Things” over network

## Slide 8
मैं अरदुनओ हूँ
我的Arduino!
Je suis Arduino
나는 아두 이노입니다
Ik ben Arduino!
Sono Arduino!
I am Arduino!

## Slide 9: Activity #1
Build a light with a switch you push to turn it on (Just like the one for door-bell)
Try with the Latch (an On-Off switch, just like one for light)
Notes: 00:10

## Slide 10: What do you need?
Red L-E-D
Push to On
Switch
Resistor (100 ohms)
2 AA Batteries
Battery Holder
Wires
1 Red
1 Black
Breadboard
Brown Ring
Black Ring
Brown Ring
Latch

## Slide 11: Go build !
Let’s Build !
Long leg

## Slide 12: Did it work?

## Slide 13: Did you try with the other type of switch?
What is the difference?

## Slide 14: Electricity
Atom and sub-atomic particles
  Electrons (negatively or –ve charged)
  Protons (positively or +ve charged )
Electric charge
Electric force
Electricity
Animations to check out: http://scratch.mit.edu/users/Devoxx4Kids-USA/
Notes: http://scratch.mit.edu/users/Devoxx4Kids-USA/
Battery Sketches
Electric charge is the physical property of matter that causes it to experience a force when close to other electrically charged matter. There are two types of electric charges – positive and negative. Positively charged substances are repelled from other positively charged substances, but attracted to negatively charged substances; negatively charged substances are repelled from negative and attracted to positive. An object will be negatively charged if it has an excess of electrons, and will otherwise be positively charged or uncharged.
Electricity is the set of physical phenomena associated with the presence and flow of electric charge. Electricity gives a wide variety of well-known effects, such as lightning, static electricity, electromagnetic induction and electrical current. In addition, electricity permits the creation and reception of electromagnetic radiation such as radio waves.

## Slide 15: How does it work?
Water flow
Electric
Current
Pressed
Pressed
Light
Glows!

## Slide 16: What does switch do?
No current
Released
Button
Released
No light!

## Slide 17: Why do we need the resistor?
Reduced
Water flow
Lower Electric
Current
Pressed

## Slide 18: Electric push (Voltage)
> Voltage is the push for the charge to flow
> Voltage is measured in Volts
> Volts is shown as ‘V’ in diagrams

## Slide 19: Electric Current
> Current is the flow of electric charge
> Current is measured in Ampere
> Ampere is shown as Amp or A in diagrams
> Smaller unit of current is milli Ampere (or mA).
> 1000 milli Ampere = 1 Ampere

## Slide 20: Resistance
> Resistance is the opposition to the passage of electric current
> Resistance is measured in Ohms.
> Resistance is shown as Ohms or Ω
in diagrams. Larger resistances are shown as “Kilo” or “Mega”

## Slide 21: Let us meet the components ….

## Slide 22: I am battery
> I push the electrons or “electric charge” in the circuit
> Each battery provides a push for electrons to
flow.
> The push is also called Voltage and is measured in Volts.
> Each AA Battery provides 1.5 Volts of push.
> Two batteries pushing after one another
create a push of 3.0 volts
Notes: Low voltage
Never play with the main outlets

## Slide 23: I am L-E-D
> An LED is a very small light, often colored (white / red / yellow / green)
> Each LED has two legs ... a short and a long
> Long is the PLUS (+) (positive pole)
> It glows when current flows
> It can handle only small amount of current
> Short ... MINUS (-) (Negative pole)

## Slide 24: I am resistor
> I offer resistance to the flow of current
> The amount of resistance I offer is fixed.
> The amount of resistance I offer is measured in Ohms. Sometimes people prefer to use Kilo and Mega Ohms to keep the numbers small and easily readable
> The amount of resistance I offer is identified by the colors of the rings on me.
Resistor (100 ohms)
Brown (1)
Ring
Black (0)
Ring
Brown (1)
Ring
1 0 0 Ohms
Notes: Try the scratch

## Slide 25: How much is my resistance?
First Digit
Second Digit
Multiplier
Tolerance
A
B
C
D

## Slide 26: I am “Push for On” switch
> I let current pass when you press me.
> I do not let any current to flow when I am left alone.

## Slide 27: I am Push Button Latch
> Press me to close the circuit (“On”)
> Press again to open the circuit
(“Off”)

## Slide 28: I am wire
> I am the pipe thru which electrons flow from one component to another.
> I do not change the flow/ offer resistance.
> What ever voltage is one end, it gets transferred to the other end.
> Color of the insulation does not change what I do!
> Color can help identifying what signal I have, if you follow convention. For example, red color in usually the +ve voltage while black is Ground.

## Slide 29: I am Breadboard

## Slide 30: Go build !
Under the breadboard hood
Long leg

## Slide 31: The circuit diagram
3.0 Volt
100 Ω
… in the language of the engineers !
10 milli Ampere

## Slide 32: The circuit diagram
3.0 Volt
100 Ω
… in the language of the engineers !
10 milli Ampere

## Slide 33: Which picture will you use to help a friend drive from Redwood City to Mountain View?

## Slide 34: Activity #2
Build a light with a Dimmer
Notes: 00:40

## Slide 35: What do you need?
Red L-E-D
10 Kilo Ohm variable resistor
Aka Potentiometer
Resistor (100 ohms)
2 AA Batteries
Battery Holder
Wires
1 Red
1 Black
Breadboard
Brown Ring
Black Ring
Brown Ring

## Slide 36
Let’s build ..…
Long leg

## Slide 37: Did it work?

## Slide 38: Let us meet the components ….

## Slide 39: I am the variable resistor
> I have three terminals
> I offer fixed resistance between the two end terminals.
> Resistance between the middle terminal and either of the two end terminal depends upon where the know is turned.
> The amount of resistance is somewhere in between fixed resistance and zero.

## Slide 40: The circuit diagram
3 Volt
10 K Ω
… in the language of the engineers !
100 Ω

## Slide 41: How does it work?

## Slide 42: Ohm’s Law
If we increase the resistance in the circuit, less current will flow thru it.
Provided we do not change the voltage ( push).
Notes: Check out the scratch

## Slide 43: Ohm’s Law
If we increase the push(voltage) applied to the circuit, more current will flow thru the circuit
Provided we do not change the resistance

## Slide 44: Ohm’s Law
Voltage drop across a component is the amount of current flowing through it and multiplied by the resistance offered by it.
V = I * R

## Slide 45: What do we use Ohm’s law for?
> LED manufacturer says: “This LED may be damaged if current above 10 milli Amps flows thru it. The voltage across the red LED will be 2 volts when it is glowing.”

## Slide 46: Please remove the batteries
Why?

## Slide 47: Activity #3
Blinking LED using Arduino
Notes: 00:55
Stretch

## Slide 48: What do you need?
Red L-E-D
Resistor (270 ohms)
Arduino
Wires
1 Red
1 Black
Breadboard
Brown Ring
Violet Ring
Red Ring
Laptop
USB cable

## Slide 49: How does it work?
Sensing
Controlling
Input
ports
Output
ports
Instructions

## Slide 50: Digital Output Port
Device (our LED circuit) is connected to the port
Arduino generates signal on the port
The device receives the signal and acts
Example: Signal on the port is set to 5 Volts to “Power-On” the LED
Start
Turn
On
Turn
Off
Turn
On
Turn
Off
Turn
On
5 Volts
0 Volts
Wait
1 second
Wait
1 second
Wait
1 second
Wait
1 second

## Slide 51: Let’s meet the components ….
Port 13
GND (Ground)
USB
Port

## Slide 52: The circuit diagram
270 Ω
… in the language of the engineers !
9 milli Ampere
13
GND
Arduino

## Slide 53
Let’s build!
Long leg
Connect USB cable
Connect – ve of Board To GND on Arduino
Connect +ve of Board to Port 13 on Arduino

## Slide 54: Time to write a “Sketch”

## Slide 55: Did you download and install the software successfully? If not …
Go http://arduino.cc/en/Main/Software
Download the software appropriate for your computer
  Windows 7
  Windows 8
  Mac
  Linux
Install the software on you computer
64 bit Windows – manually install Driver using Device Manager.

## Slide 56: Install the driver (Windows only)
Open Windows explorer and navigate to “Computer” and right click on it.
Select “Properties”
Click on “Device Manager”
Look under Ports (COM & LPT). Mostly likely you will find the Arduino as COM3 or COM4.
Right click and choose to “Update Driver Software”
Select “Browse my computer for software driver”
Select the appropriate driver from the “drivers” directory of the Arduino software you had downloaded. (e.g. ….arduino\arduino-1.0.5\drivers )

## Slide 57: Is Arduino connected the computer?
Time to get them talking ….

## Slide 58: Outline of the Sketch: Please Arduino ….
Use Port 13 for output
Set Port 13 voltage = 5 Volts (Glow the LED)
Wait for 1 second
Set Port 13 voltage = 0 Volt (Switch-off LED)
Wait for 1 second
Keep repeating the Steps 2 to 4 forever

## Slide 59: Select Board “Arduino Uno”

## Slide 60: Select the Communication Port (Windows)

## Slide 61: Select the Communication Port (Mac)

## Slide 62: Write the Sketch
Click on Upload to send the instructions from the computer to Arduino
Verify instructions were
Uploaded!!
And there were no errors
........

## Slide 63: Sketch
int ledPort = 13 ;
void setup()
{
pinMode(ledPort, OUTPUT);
}
void loop() {
digitalWrite(ledPort, HIGH);
delay(1000);
digitalWrite(ledPort, LOW);
delay(1000);
}
Notes: Setup – called one time
INPUT or OUTPUT
Loop – continuously repeated
HIGH – 5V
LOW – 0V
Why do we use ledPort?
Why do we use Camel Case?

## Slide 64: Did it work?

## Slide 65: Talking to the world
On
Off
On
Off
Input Port
Output Port

## Slide 66: Digital Input Port
Signal on the port is measured as either 0 or 1. It can only be one of the two values.
Example
  If voltage on the port is 5 V, it is On (Binary 1)
  If voltage on the port is 0 V, it is off (Binary 0)