## Slide 1: Activity #5 Automatic Eco Light
LED does not glow when the surrounding has fair amount of light.
LED glows when it gets dark
The glow intensity increases as it gets darker

## Slide 2: Keep the circuit you build for next activity!

## Slide 3: What do you need?
Resistor (10 Kilo ohms)
Arduino
Breadboard
Orange Ring
Black Ring
Brown Ring
Laptop
USB cable
White LED
Brown Ring
Black Ring
Brown Ring
Resistor (100 ohms)
Light
Dependent
resistor (LDR)

## Slide 4: I am Light Dependent Resistor ….
You can call me LDR
When there is light, my resistance is low
  More current flows thru me
When it is dark my resistance is high
  Less current flows thru me

## Slide 5: Circuit Diagram
9 5V
A0
GND
Arduino
100 Ω
W
10K Ω

## Slide 6
LED
LDR
10K Ω
100 Ω

## Slide 7
Let’s build!
Long leg
Connect orange wire to Port 9 of Arduino
Connect Green wire to Port A0 of Arduino
Connect –ve (Black Wire) to GND of Arduino
Connect +ve (Red Wire) to 5V of Arduino
To -ve
To +ve
Connect brown wire to -ve

## Slide 8
Let’s build!
Connect USB cable
To computer
Connect 5V to +ve of Board
Connect LDR to Port A0
Connect
GND to
-ve of
Board
Connect Port 9 to LED’s resistor

## Slide 9: Sketch – Part 1
const int LED_PORT = 9 ;
const int LIGHT_SENSOR_PORT = 0 ;
const int INTERVAL = 1000 ; // we will check brightness 1000 millisecond or 1 second
int sensedValue ; // value sensed on the Analog input port
float voltage ; // a number between 0 and 5 Volts
float light ; // a number between 0 and 1, 0 means very dark, 1 means bright
float darkness ; // a number between 0 and 1, 1 means it is very dark)
float needLight ;
int setLEDTo ; // value to output on the analog port for LED
Notes: Copy the sketch if you want to …. Copy the folder to Arduino directory.

## Slide 10: Sketch – Part 2
void setup() {
pinMode(LED_PORT, OUTPUT);
pinMode(LIGHT_SENSOR_PORT, INPUT);
Serial.begin(9600) ;
for (int i = 0; i<=255 ; i++ ) {
analogWrite (LED_PORT,i);
Serial.println(i);
delay (100);
}
analogWrite (LED_PORT, 0);
delay (100);
}

## Slide 11
void loop() {
sensedValue = analogRead(LIGHT_SENSOR_PORT) ;
// read the input on analog port
// Convert the analog reading (which goes from 0-1023) to a voltage (0-5V):
// Voltage will only go from 0.4 to 2.5 approximately only
voltage = sensedValue * 0.0049 ;
light = sensedValue / 1023.0 ;
darkness = 1 - light ;
if ( darkness > 0.5 ) needLight = ( darkness - 0.5 ) / ( 1 - 0.5 );
else needLight = 0 ;
setLEDTo = 255 * needLight ;
analogWrite (LED_PORT,setLEDTo);
Serial.print("Sensor Value = "); Serial.print(sensedValue);
Serial.print(" Voltage ="); Serial.print(voltage);
Serial.print(" Light ="); Serial.print(light);
Serial.print(" Darkness ="); Serial.print(darkness);
Serial.print(" need light ="); Serial.print(needLight);
Serial.print(" Set LED port to ="); Serial.println(setLEDTo);
delay (INTERVAL);
}

## Slide 12: Keep the circuit you build for next activity!

## Slide 13: Analog Input Port
Signal on the port is measured as a number between 0 and 1023
Example
  If voltage on the port is 5 V, value of the input is measured as 1023
  If voltage on the port is 2.5 V, value of the input is measured as 612
  If voltage on the port is 0 V, value of the input is measured as 0

## Slide 14: Analog Output Port
Signal of value between 0 and 255 can be sent out. 0 means 0 Volts. 255 means 5 Volts.
Example
  If 255 is written to the output port, signal on the pin goes to 5 Volts.
  If 123 is written to the output port, signal on the pin goes to 2.5 Volts.
  If 0 is written to the output port, signal on the pin goes to 0 Volts.

## Slide 15: How does it work?
9 5V
A0
GND
Arduino
100 Ω
W
10K Ω
LDR offers resistance of about 2500 ohms
Voltage across 10 Kilo Ω Resistor is about 4 volts
Current flowing 0.4 milli Amps
2K Ω
Arduino senses a value of about 800
on the Analog input port A0
Bright
Lot’s of light !
Notes: Show the sketch

## Slide 16: How does it work?
9 5V
A0
GND
Arduino
100 Ω
W
10K Ω
LDR offers resistance of about 500,000 ohms
Voltage across 10,000 ohm resistor drops to about 0.01 volts
Current flowing drops to about 0.001 milli Amps
500K Ω
Arduino senses a value of about 2
on the Analog input port A0
Dark . No light!

## Slide 17: Activity #6 Remote controlled light
Re-use the light sensor and LED circuit we built earlier
Instead of Arduino automatically switching on or off the LED, this time we will control it over the network.
We will check the lighting situation around our sensor from another computer
Turn On or Turn Off the LED by sending command from another computer.

## Slide 18: What are we going to build?
Scratch Program
S4AFirmware program

## Slide 19: Circuit Diagram
9 5V
A0
GND
Arduino
100 Ω
W
10K Ω

## Slide 20: Did you download and install the Scratch4Arduino?If not …
Go http://s4a.cat/
Download the software appropriate for your computer
  Windows
  Mac
  Linux
Install Scratch4Arduino

## Slide 21: Installing S4A on Mac
S4A installation on Mac needs work around:
  Security permissions need to be changed to "Anywhere" in order to open the app.
  https://groups.google.com/forum/#!topic/s4a-community/5e_ge7XKehw

## Slide 22: Load the S4A Firmware sketch to the Arduino
Locate the file S4AFirmware15.ino
Run Arduino software
Open the sketch S4AFirmware15.ino
Connect Arduino and upload the sketch to Arduino board using Arduino software
Make sure it loaded successfully!
Exit the Arduino software once done!

## Slide 23: Load the S4A Firmware sketch to the Arduino

## Slide 24: Connect to wireless network “devoxx4kids”

## Slide 25: Run Scratch 4 Arduino

## Slide 26: Open the project LightController
Navigate to Menu : File > Open
Find, select and open the file LightController

## Slide 28: “LightController” project
Arduino is connected to the computer.
The message “Searching for board” should go away
Did you see the message “Remote Sensor Connections Enabled”?
Are the variables showing running numbers?

## Slide 29: Have you used Scratch?

## Slide 30: What is Scratch?
Scratch is a programming environment where you can create your own interactive stories, games, and animations
You can use it on internet or you can download and run it on your computer
We will download and run on the computer
Info and downloads at: http://scratch.mit.edu/

## Slide 31: What is Scratch for Arduino?
S4A is a Scratch modification that allows for simple programming of the Arduino.
It provides new blocks for managing sensors and actuators connected to Arduino.

## Slide 33: Enable remote sensor connection
> Click on “Sensing” Block Palette
> Right click on one of the blocks, “help” menu will open.
> Click on enable remote sensor connections.

## Slide 34
> Click on the green flag
to start the program
> Did the LED Blink 5 times?

## Slide 35: Note the IP address of your computer
> Click on menu “Edit” > “Show IP Address”
> Note down the IP Address displayed

## Slide 36: Command to check light around sensor
http://192.168.0.106:42001/?send_vars

## Slide 37: Commands to turn on or off the LED
http://192.168.0.106:42001/vars-update=Command=On
http://192.168.0.106:42001/vars-update=Command=Off

## Slide 38: How does it work?
Scratch Program
Network

## Slide 39: Let’s meet the Arduino again ….
I/O pins
Power pins
USB
Port
Analog input pins
7-12V
DC input
ATMega328 MC
LEDs
Reset pin

## Slide 40: Books
Exploring Arduino by Jeremy Blum
Programming Arduino Getting Started with Sketches
Programming Arduino Next Steps by Simon Monk
Arduino Cookbook by Michael Margolis

## Slide 41: Useful websites
Arduino reference www.arduino.cc/en/Reference/HomePage
Arduino forum www.arduino.cc/forum
Ideas for projects http://www.instructables.com/
Ideas for projects http://makezine.com/
http://www.allaboutcircuits.com/
http://www.wikipedia.org/