## Slide 1: Let us make our second device
What?
  Smart light that will glow when it gets dark
  Stops glowing when it is not dark
Why?
  Understand Sensor, Actuator, Controller
  Learn about Input / Output Pins Arduino uses to talk to the sensors and actuators.
  Learn how to provide instructions (also called “Sketch”) for Arduino that provide the behavior to the device
Notes: + 45 minutes
Break??
Activity #2 Introduction – 10 minutes

## Slide 2: Sensors
Sense the world.
Examples:
  Light sensor
  Sound sensor
  Temperature sensor
  Location (GPS)
  Orientation sensor
  Distance sensor

## Slide 3: Actuators
Change the world
Examples:
  LED – bring light
  Speaker - sound
  Motor – Move
  Relays/Switches
  Robotic arm - Move

## Slide 4: How does Arduino talk to sensors and actuators?
On
Off
Input pins
sense voltage
Output pins
provide voltage
On
Off
5Volt = 1 5Volt = 1023
0Volt = 0 0Volt = 0
1 = 5Volt 255 = 5Volt
0 = 0Volt 0 = 0Volt

## Slide 5: How does the device work?
Light Sensor
Actuator
Input pin
Output pin
Instructions

## Slide 6: Digital Output Pin
Device (our LED circuit) is connected to the output pin
Arduino generates signal on the pin
The device receives the signal and acts
Example: Signal on the port is set to HIGH (5 Volts) to “Power-On” the LED
Start
Turn
On
Turn
Off
Turn
On
Turn
Off
5 Volts
0 Volts

## Slide 7: Analog Input Port
Signal on the port is measured as a number between 0 and 1023
Example
  If voltage on the port is 5 V, value of the input is measured as 1023
  If voltage on the port is 2.5 V, value of the input is measured as 612
  If voltage on the port is 0 V, value of the input is measured as 0
Notes: + 55 minutes
Activity #2 Building 25 minutes

## Slide 8: Step 1: Assemble the components on the breadboard

## Slide 9: The wiring diagram
9 Volt
LED
LED
270 Ω
10KΩ
LDR

## Slide 10: Insert the LED on breadboard
Insert long leg in d3
Insert short leg in d5
+ Rail inward

## Slide 11: Insert the 270 Ohm resistor
Insert one leg in a5
Insert other in a21

## Slide 12: Insert the 270 Ohm Resistor
Insert one leg in a5
Insert other leg in a21

## Slide 13: Pick, bend and insert 10Kilo Ohm resistor
Insert one leg in g26
Insert other leg in g11
Black Ring
Brown
Ring
Orange Ring

## Slide 14: Pick & insert the Light Dependent Resistor (LDR)
Insert one leg in f26
Insert other leg in f29

## Slide 15: Breadboard should look like ….

## Slide 16: Step 2: Connect wires on the breadboard
> Use shorter wires for connecting components on the board

## Slide 17
Connect Minus rail to i11 blue wire
Connect Minus rail to c21 using blue wire
Connect Plus rail to j29 using red wire

## Slide 18: Step 3: Connect wires between breadboard and Arduino
> Use longer wires for connecting the board to Arduino

## Slide 19: Connect pin 9 on Arduino to e3 on breadboard using orange wire

## Slide 20
> Connect pin A0 to i26 using green wire
> Connect pin 5V on Arduino to Plus Rail on breadboard using red wire
> Connect pin GND on Arduino to Minus Rail on breadboard using blue wire

## Slide 21: Step 4: Write instructions and upload to Arduino

## Slide 22: Connect Arduino to the computer
> USB
Connector
> USB cable
> To computers USB
Port

## Slide 23: Make sure Windows detects Arduino correctly
Click on Windows logo at bottom left corner of the screen
Click on “Devices and Printers”
Arduino Uno should be listed there.
Note the port. Example COM17 in this image.

## Slide 24: Open Arduino IDE
Click on the Arduino icon on your desktop
A window like this should open up
Arduino

## Slide 25: What is integrated development environment or IDE?
This is the place where you write instructions for the Arduino
It checks the instructions can be understood by Arduino
Passes the “Sketch” to Arduino (“Upload”)
Allows us to chat with Arduino if needed.

## Slide 26: Select Board “Arduino Uno”

## Slide 27: Select the Communication Port the computer uses to send the instructions to Arduino and talking to it.
Port you had noted earlier should be visible here.
Select it

## Slide 28: Write the instructions (also called “Sketch”)
Click on menu option “File” in the Arduino IDE
Select “Sketchbook”. Select “Smart_light”.
The instructions similar to those in the next three slides will show up in the window
I have pre-written them to save time. In real life you will have to write them.
The programming language used is similar to C++.

## Slide 29: Sketch Part 1
/*
Automatic light
Arduino is connected to a light sensor and a LED.
Arduino switches the LED on when it becomes somewhat dark.
It switches the LED off when it is bright.
by Pradeep Bhatter
*/
/* Use pin 9 to signal the LED */
const int LED_PIN = 9 ;
/* Use pin 0 for reading the level of brightness from the light sensor */
const int LIGHT_SENSOR_PIN = 0 ;
/* time the controller should wait before resensing - 1000 millisecond or 1 second */
const int INTERVAL = 1000 ;
/* Box to store the value read from brightness sensor */
int sensedValue ;
Notes: Setup – called one time
INPUT or OUTPUT
Loop – continuously repeated
HIGH – 5V
LOW – 0V
Why do we use ledPort?
Why do we use Camel Case?

## Slide 30: Sketch Part 2
void setup() {
/* My Dear Arduino, */
/* Use pin 9 for telling the LED to glow or not */
pinMode(LED_PIN, OUTPUT);
/* Use pin 0 to read the level of brightness from the light sensor */
pinMode(LIGHT_SENSOR_PIN, INPUT);
/* If connected to computer, set the speed to talk to it at 9600 bits/second */
Serial.begin(9600) ;
/* Tell the computer you are ready to roll */
Serial.println("Ready to roll ....");
delay (100);
}

## Slide 31: Sketch Part 3
void loop() {
/* My Dear Arduino,
Keep doing what I telling you here ….
*/
/* Read the strength of the signal on pin connected to light sensor */
sensedValue = analogRead(LIGHT_SENSOR_PIN) ;
/* Read the pin light sensor is connected to.
If the value read is less than 400, set LED pin to 1. It will make the LED glow.
Otherwise, set the LED pin to 0. It will make the LED turn off.
*/
if (sensedValue < 400)
digitalWrite(LED_PIN, HIGH) ;
else
digitalWrite(LED_PIN, LOW) ;
/* Tell the computer, the value you read from light sensor */
Serial.print("Sensor Value = ");
Serial.println(sensedValue);
/* Wait and then go again ... */
delay (INTERVAL);
}

## Slide 32: Upload the sketch to Arduino
Click on Upload to send the instructions from the computer to Arduino
Verify instructions were
Uploaded!!
And there were no errors
........

## Slide 33: Open a chat window with the Arduino
Click on “Serial Monitor” in “Tools” menu.

## Slide 35: Show time!
Does chat window show the message from Arduino “Ready to roll …”
Does the chat window show the sensor value?
Go cover the sensor with your hand. Does the value change as you increase/decrease the light falling on the sensor? (if not, something is wrong. Call for help!)
Does it fall below 400 when you cover the light sensor? (if not, you may have to change and upload again.)
If the value falls below 400, does the LED glow?
Notes: + 1:25
Activity #2 Explain code – 10 minutes

## Slide 36: Did it work?

## Slide 37: Time for Arduino to take a break
Switch off the battery by sliding the switch to off
Disconnect the battery from Arduino
Remove all components from the bread board and pack them back neatly into the box.

## Slide 38: Let us meet the new components ….

## Slide 39: I am Light Dependent Resistor ….
You can call me LDR
When there is light, my resistance is low
  More current flows thru me
When it is dark my resistance is high
  Less current flows thru me

## Slide 40: Software (or Sketch)

## Slide 41: Sketch Part 1
/*
Automatic light
Arduino is connected to a light sensor and a LED.
Arduino switches the LED on when it becomes somewhat dark.
It switches the LED off when it is bright.
by Pradeep Bhatter
*/
/* Use pin 9 to signal the LED */
const int LED_PIN = 9 ;
/* Use pin 0 for reading the level of brightness from the light sensor */
const int LIGHT_SENSOR_PIN = 0 ;
/* time the controller should wait before resensing - 1000 millisecond or 1 second */
const int INTERVAL = 1000 ;
/* Box to store the value read from brightness sensor */
int sensedValue ;
Notes: Setup – called one time
INPUT or OUTPUT
Loop – continuously repeated
HIGH – 5V
LOW – 0V
Why do we use ledPort?
Why do we use Camel Case?

## Slide 42: Sketch Part 2
void setup() {
/* My Dear Arduino, */
/* Use pin 9 for telling the LED to glow or not */
pinMode(LED_PIN, OUTPUT);
/* Use pin 0 to read the level of brightness from the light sensor */
pinMode(LIGHT_SENSOR_PIN, INPUT);
/* If connected to computer, set the speed to talk to it at 9600 bits/second */
Serial.begin(9600) ;
/* Tell the computer you are ready to roll */
Serial.println("Ready to roll ....");
delay (100);
}

## Slide 43: Sketch Part 3
void loop() {
/* My Dear Arduino,
Keep doing what I telling you here ….
*/
/* Read the strength of the signal on pin connected to light sensor */
sensedValue = analogRead(LIGHT_SENSOR_PIN) ;
/* Read the pin light sensor is connected to.
If the value read is less than 400, set LED pin to 1. It will make the LED glow.
Otherwise, set the LED pin to 0. It will make the LED turn off.
*/
if (sensedValue < 400)
digitalWrite(LED_PIN, HIGH) ;
else
digitalWrite(LED_PIN, LOW) ;
/* Tell the computer, the value you read from light sensor */
Serial.print("Sensor Value = ");
Serial.println(sensedValue);
/* Wait and then go again ... */
delay (INTERVAL);
}

## Slide 44: Circuit Diagram
9 5V
A0
GND
Arduino
270 Ω
W
10K Ω
Notes: + 1:35 minutes

## Slide 45: How does it work?
9 5V
A0
GND
Arduino
100 Ω
W
10K Ω
LDR offers resistance of about 2500 ohms
Voltage across 10 Kilo Ω Resistor is about 4 volts
Current flowing 0.4 milli Amps
2K Ω
Arduino senses a value of about 800
on the Analog input port A0
Bright
Lot’s of light !
Notes: Show the sketch

## Slide 46: How does it work?
9 5V
A0
GND
Arduino
100 Ω
W
10K Ω
LDR offers resistance of about 500,000 ohms
Voltage across 10,000 ohm resistor drops to about 0.01 volts
Current flowing drops to about 0.001 milli Amps
500K Ω
Arduino senses a value of about 2
on the Analog input port A0
Dark . No light!

## Slide 47: Demo (if time permits) Remote controlled light
Uses the light sensor and LED circuit we built earlier
Instead of Arduino automatically switching on or off the LED, this time we will control it over the network.
Turn On or Turn Off the LED by sending command from another computer.

## Slide 48: Connect to wireless network “devoxx4kids”

## Slide 49: Use browser on your computer to send these commands …
http://192.168.0.126:42001/vars-update=Command=On
http://192.168.0.126:42001/vars-update=Command=Off
http://192.168.0.126:42001/vars-update=Command=On=Name=Pradeep
http://192.168.0.126:42001/?send_vars

## Slide 50: How does it work?
Scratch Program
Network

## Slide 51: Let’s meet the Arduino again ….
I/O pins
Power pins
USB
Port
Analog input pins
7-12V
DC input
ATMega328 MC
LEDs
Reset pin

## Slide 52: Joining hands …
Internet of Things
Sensors
Controllers
Wireless &
Network
Apps
Mobile devices
Cloud

## Slide 53: Books
Exploring Arduino by Jeremy Blum
Programming Arduino Getting Started with Sketches by Simon Monk
Programming Arduino Next Steps by Simon Monk
Arduino Cookbook by Michael Margolis
The Art of Tinkering by Karen Wilkinson and Mike Petrich
Getting Started with Arduino by Massimo Banzi
The Design of Everyday Things by Donald A. Norman

## Slide 54: Useful websites
Arduino
  Comic http://playground.arduino.cc/Main/ArduinoComic
  http://arduino-info.wikispaces.com/
  Reference www.arduino.cc/en/Reference/HomePage
  Forum www.arduino.cc/forum
Ideas for projects
  http://www.instructables.com/
  http://makezine.com/
Excellent tutorial on Electricity, Circuits
  http://www.allaboutcircuits.com/
  http://www.wikipedia.org/
  https://learn.sparkfun.com/tutorials/what-is-electricity

## Slide 55
मैं अरदुनओ हूँ
我的Arduino!
Je suis Arduino
나는 아두 이노입니다
Ik ben Arduino!
Sono Arduino!
I am Arduino!
Thank you
  O'Reilly Media
  Allison Gillespie - O'Reilly Media
  Andrew King & team
  O’Reilly OSCON Team
  Welden, Robert and other parents